## Slide 1: CBETA Field maps of the FFAG magnets and beam optics results of the FFAG cell from Zgoubi
N. Tsoupas, F. Méot
Zgoubi workshop August 25 to 30 2019

## Slide 3: Outline
What the CBETA is.
What the field maps are.
  Generation of field maps.
  How the field maps are used.
Some results of the optical functions of CBETA as calculated by Zgoubi using field maps.

## Slide 4
Injection: 6 MeV e- 100 mA rep-rate 325 MHz
1.3 GHz 16 MV/m Emax~80 MeV
Beam dump
Splitter
Merger
Two remarkable concepts:
Energy Recovery Linac (ERL)
Fixed Field Alternating Gradient (FFAG)
Pass # | Energy
1 | 42
2 | 78
3 | 114
4 | 150
5 | 114
6 | 78
7 | 42
8 | 6
What is CBETA?

## Slide 5: The CBETA project is a prototype for the eRHIC project
Injection: 6 MeV e- 100 mA rep-rate 325 MHz
1.3 GHz 16 MV/m ~80 MeV
Beam dump
Splitter
Merger
Two concepts: Energy Recovery Linac (ERL)
Fixed Field Alternating Gradient (FFAG)
Pass # | Energy
1 | 42
2 | 78
3 | 114
4 | 150
5 | 114
6 | 78
7 | 42
8 | 6
At any given time there is an equal number of accelerating
and decelerating bunces inside the ERL.
The Power of the ERL is minimal

## Slide 6: The concept of the FFAG cell
41 mm
Focusing
Quad
DeFocusing
Quad
Trajectories of e-bunches with different energy
A large energy range (42 MeV to 150 MeV) is confined in a small transverse distance of 41 mm

## Slide 7
Realization of five FFAG cells on a girder
OPERA design of 3 cells
with Correctors
Single Halbach Magnet
with Corrector

## Slide 8
Perspective view of Magnetized Wedges
Cross section of Magnetized Wedges of NdFeB or SmCo

Direction of the easy axis =(n+1) +/2
Dipole n=1
Quad n=2
Sext n=3

The Halbach Quadrupole

## Slide 9: Large fields in small volume magnet
Gap=3 cm W=30 cm H=18 cm Bmax~ 1 Tesla
Needs Power Supply and water for cooling
ri
rout

## Slide 10: Halbach Magnets do not interfere NO-Cross-talk
+
Halbach Quadrupole
Halbach Dipole
Dipole, Quadrupole combination
Permanent magnet material is saturated (1)
The field of one magnets will add to that of the other

## Slide 11: Wire-Correction of harmonics

## Slide 12: Correctors

## Slide 18: Thank you for your attention

## Slide 19: The splitter of the CBETA accelerator
S2.BEN01
ERL
FFAG
150 MeV
114 Mev
78 MeV
42 MeV
Beam Dump Line
S1.BEN01
S4.BEN01

## Slide 20
Trajectory of 114 MeV
Trajectory of 150 MeV
Magnet cross section Normal
to the beam direction
Coil
Coil
Iron
Vacuum pipe for 114 MeV
Walls of vacuum chamber for 150 MeV
Magnet cross section along the
median plane to the magnet
The trajectories of the 114 MeV and 150 MeV beams at the location of the
S4.BEN01 dipole magnet.

## Slide 21: B/B~5x10-4
B<9 mGauss

## Slide 22: Why do we propose an alterative magnet?
Length [m] | Bfield [T] | Bend angle | Sagitta [cm] | Gap [cm] | Septum [cm] | Hor. Aper. [cm] | Current [A.turns] | J [A/cm2]
0.2 | 0.40617 | 9.3o | 0.2 | 3.4 | 2.68 | 3.5 | 10990 | 1400
Table A2. S4.BEN01 Magnet specifications
This magnet with the power supply will cost more than $150K

## Slide 23
Isometric view of Magnetized Wedges
Cross section of Magnetized Wedges of NdFeB or SmCo
The Halbach type Magnet
The Halbach magnet

Direction of the easy axis =(n+1) +/2
Dipole n=1
Quad n=2
Sext n=3

=direction of the easy axis
=azimuthal angle of the wedge

## Slide 24: Dipole field
Gap=3 cm W=30 cm H=18 cm Bmax~ 1 Tesla
Electromagnet Needs High current Supply
ri
rout
Quadrupole field n=2

## Slide 25: Field Uniformity of Halbach magnet (2D)
B/B~5x10-4

## Slide 26: Field Uniformity of Halbach magnet (3D)
Length [m] | Bfield [T] | Sagitta [cm] | Rin [cm] | Rin [cm] | PM Material | Br [T] | Hc [A/m]
0.12 | 0.30 | 0.12 | 2.0 | 3.5 | NdFeB_N35EH | 1.2040 | -147.03
Table 3. The S4.BEN01 modified Halbach-type magnet specifications

## Slide 27: Modified Halbach magnet to reduce radiation damage

## Slide 28: Isometric views of the Halbach magnet followed by a low field corrector electromagnet
Low field
corrector magnet
Vacuum pipe of
magnetized material
114 MeV
150 MeV

## Slide 29: Conclusions Halbach vs electromagnet
The Halbach magnet occupies smaller volume and can generates higher field in the same aperture.
It costs much less then the electromagnet.
It can be temperature controlled by water cooling.
It is subject to radiation damage.
  This is not a serious problem in the environment of 150 MeV electrons.
  The magnet will also be shielded for radiation damage.

## Slide 30: Thank you for your attention